LHC COLLIMATOR TRANSVERSE IMPEDANCE

L. Vos

1 INJECTION

D. Angal, L. Vos, Coupled Bunch Instabilities in the LHC, EPAC 2002 :

Budget transverse impedance (resistive, H,V)

45		57 M/m

Includes contribution single graphite collimator (estimated aperture and ) :

0.3		1.1 M/m

Impedance of all graphite collimators with correct aperture and  (2003):

13.3		16.8 M/m

New total :

58		73 M/m

# Can be handled by transverse feedback

2 HIGH ENERGY

D. Angal, L. Vos, Coupled Bunch Instabilities in the LHC, EPAC 2002 :

Budget transverse impedance (resistive, H,V)

84		118 M/m

Includes contribution single graphite collimator (estimated aperture and ) :

2.2		7.9 M/m

Impedance of all graphite collimators with correct aperture and  (2003):

841		1017 M/m

New total :

923		1127 M/m

So what ?

Collisions

## Feedback OFF

## stability by Landau damping, margin : factor ~4

### No collisions

Operational complication : increase feedback gain G by factor ~10 before collimators close

No effect specifically related to increase in gain or ZT

Steer beams into collisions

#### Feedback ON with high gain

L. Vos, Transverse Emittance Blow-up from Dipole Errors in Proton Machines, EPAC 1998

L. Vos, Damping of Coherent Oscillations, NIM 1997

- a) feedback active (Landau damping insufficient)

emittance blow up proportional with tune spread (independent of G)

- b) feedback not active but still ON (Landau damping sufficient)

emittance blow up proportional with G2

but much smaller than a) even for extreme G=0.01

### Conclusion

FEEDBACK GAIN (~ZT) HAS NO EFFECT ON EMITTANCE AT 7 TEV/C